## Slide 1
Lubrication

## Slide 2
Reduces friction and wear between moving parts
Transfers heat away from engine parts
Cleans the inside of the engine
Cuts power loss and increases fuel economy
Absorbs shock between moving parts
Lubrication System
Functions

## Slide 3
Components:
  engine oil
  oil pan
  pressure relief valve
  oil filter
  oil galleries
Lubrication System
Operation

## Slide 4: Typical Lubrication System

## Slide 5: System Components

## Slide 6: Operation
Oil pump pulls oil out of the pan
Pickup screen removes large particles
Pump pushes oil through the oil filter and galleries
Oil filter removes very small particles
Filtered oil flows to camshaft, crankshaft, lifters, rocker arms and other moving parts

## Slide 7: Engine Oil
Keeps moving parts from making direct contact
Reduces friction
Refined from petroleum (crude oil)
Synthetic oils are made from substances other than crude oil

## Slide 8: Oil Film
Oil film separates engine parts, preventing metal-on-metal contact

## Slide 9: Oil (Bearing) Clearance
Small space between moving parts, about .002” (0.05 mm)

## Slide 10: Bearing Types

## Slide 11: Oil Viscosity (Weight)
Thickness or fluidity of engine oil
High viscosity number - SAE 30
  thick oil
Low viscosity number - SAE 5
  thin oil
Viscosity number is printed on container (standardized by SAE)

## Slide 12: Temperature Effects
Cold oil is very thick and resists flow
When heated, oil thins and becomes runny
If it becomes too hot and thin, the oil film can break down and part contact can result

## Slide 13: Single and Multiviscosity Oils
Single viscosity—SAE 20, 30 or 40
  limited range of operating temperatures
  not as stable as multiviscosity oil
Multiviscosity—SAE 10W-30, 20W-50
  exhibits characteristics of a thin light oil when cold and a thicker, heavy oil when hot

## Slide 14: Oil Viscosity Rating
Determined by measuring how long oil takes to flow through a specific opening at a specific temperature

## Slide 15: Selecting Oil Viscosity

## Slide 16: Engine Oiling Methods
Pressure-fed oiling
  oil is provided by the oil pump to the crankshaft bearings, camshaft bearings, lifters and rocker arms
Splash oiling
  oil sprays out and on moving parts
  used between parts with moderate load such as piston rings, cylinders, and camshaft lobes

## Slide 17: Full-Flow Lubrication
System forces all of the oil through the oil filter before the oil reaches the engine
Most common type in automotive systems
Bypass Lubrication
Does not filter all of the oil
Filters some of the extra oil not needed by the bearings
Not very common

## Slide 18: Full Flow System

## Slide 19: Oil Pan and Pump

## Slide 20: Oil Pan
Oil pan forms the sump at the bottom

## Slide 21: Oil Pump
Forces oil out of the pan, through the filter and galleries, and to the engine bearings
Oil pump drives:
  shaft-driven
  belt-driven
  gear-driven
  crankshaft-driven

## Slide 22: Pressure Relief Valve
Limits maximum oil pressure
Spring-loaded bypass valve in the oil pump, engine block or filter housing
Under normal pressure conditions, a spring holds the valve closed
Under high oil pressure conditions, the valve opens, allowing some oil to pour back into the oil pan

## Slide 23: Pressure Relief Valve

## Slide 24: Oil Filters
Removes small metal particles, carbon, rust and dirt from oil
Filter element
  paper or cotton filtering substance
Filter bypass valve
  protects the engine from oil starvation
  valve opens if too much pressure is formed in the filter
  allows unfiltered oil to the bearings

## Slide 25: Oil Filter Types
Spin-on filter
  sealed unit
  filter is screwed into place
Cartridge oil filter
  separate element and housing
  to service, housing is removed
  new element is installed inside the existing housing

## Slide 26: Spin-On Oil Filter

## Slide 27: Filter Oil Flow

## Slide 28: Oil Filter Housing
Mounting place for the oil filter

## Slide 29: Oil Cooler
Heat exchanger to lower and control temperature of the engine oil

## Slide 30: Oil Galleries
Passages through the cylinder block and head for lubricating oil

## Slide 31: Oil Spray Nozzles
Direct a stream of oil onto the bottoms of the pistons, timing gears or chain
Fig 27