## Slide 1: JCT College of Engineering & Technology , Pichanur, Coimbatore -641105.
Electron Devices and Circuits
Faculty Name : J.Priyadharshni
Designation : Assistant Professor
Year/Sem : II/III
Dept : EEE

## Slide 2: Discrete Semiconductor Devices
Semiconductor Materials
  Conductor and Insulators.
  N-type, P-Type, electron, and hole current
  PN junction, depletion region, potential barrier.
Diodes
    Forward Bias, reverse bias
    Diode applications
    Light Emitting Diodes
    Zener Diodes
    Photo Diodes

## Slide 3: Conductor and Insulators. Atomic Model
the gap can be crossed
only when breakdown
conditions occur
the gap is smaller
and can be crossed
when a photon
is absorbed
the conduction band
and valence band
overlap, so there is no gap

## Slide 4: Silicon and Germanium

## Slide 5
  Conduction Electron and Holes.
An intrinsic (pure) silicon crystal at room temperature has sufficient heat energy for some valence electrons to jump the gap from the valence band into the conduction band, becoming free electron called ‘Conduction Electron’
It leaves a vacancy in valance band, called hole.
Recombination occurs when a conduction-band electron loses energy and falls back into a hole in the valence band.

## Slide 6
  Electron Hole Current.
In valance band: In valance band holes generated due to free electrons. Electrons in the valance band are although still attached with atom and not free to move, however they can move into nearby hole with a little change in energy, thus leaving another hole where it came from. Effectively the hole has moved from one place to another in the crystal structure. It is called hole current.
In conduction band : When a voltage is applied across a piece of intrinsic silicon, the thermally generated free electrons in the conduction band, are now easily attracted toward the positive end.
This movement of free electrons is one type of current in a semiconductive material and is called electron current.

## Slide 7
  Electron Hole Current.

## Slide 8
  N-type semiconductor
Electrons in the conduction band and holes in the valence band make the semiconductive material to conduct but they are too limited to make it a very good conductor..
Adding impurities in materials like Si or Ge can drastically increase the conductivity of material. The process is called doping.
Addition of a penta-valent material icnreases the number of conduction electrons.
Majority carrier: electrons
Minority carriers: holes
Material is called N-type semiconductor
An antimony
(Sb) impurity atom is shown in the
center. The extra electron from the
Sb atom becomes a free electron.

## Slide 9
  P-type semiconductor.
Trivalent impurity atom in a silicon
crystal structure. A boron (B) impurity
atom is shown in the center.

## Slide 10
  PN Junction
Although P-type material has holes in excess and N-type material has a number of free conduction electron however the net number of proton and electron are equal in each individual material keeping it just neutral.
The basic silicon structure at the instant of junction formation showing only the majority and minority carriers.
Free electrons in the n region near the pn junction begin to diffuse across the junction and fall into holes near the junction in the p region.

## Slide 11
  PN Junction
For every electron that diffuses across the junction and
combines with a hole, a positive charge is left in the n region and a negative charge is created in the p region, forming a barrier potential.
This action continues until the voltage of the barrier repels further diffusion.
The blue arrows between the positive and negative charges in the depletion region represent the electric field.

## Slide 12
  Energy band and potential barrier

## Slide 13: Diodes
Diode, semiconductor material, such as silicon, in which half is doped as p-region and half is doped as n-region with a pn-junction in between.
The p region is called anode and n type region is called cathode.
Diode symbol
Notes: Random topics just for revising some concepts.

## Slide 14: Diodes
Diode, semiconductor material, such as silicon, in which half is doped as p-region and half is doped as n-region with a pn-junction in between.
The p region is called anode and n type region is called cathode.
It conducts current in one direction and offers high (ideally infinite) resistance in other direction.
Diode symbol
Notes: Random topics just for revising some concepts.

## Slide 15: Forward Biased
  Forward bias is a condition that allows current through pn junction.
  A dc voltage (Vbais) is applied to bias a diode.
  Positive side is connected to p-region (anode) and negative side is connected with n-region.
  Vbais must be greater than ‘barrier potential’
Current limiting resistance
As more electrons flow into the depletion region reducing the number of positive ions and similarly more holes move in reducing the positive ions.
This reduces the width of depletion region.
Notes: Random topics just for revising some concepts.

## Slide 16: Reverse Biased
  Reverse bias is a condition that prevents current through junction.
  Positive side of Vbias is connected to the n-region whereas the negative side is connected with p-region.
  Depletion region get wider with this configuration.
The positive side of bias voltage attracts the majority carriers of n-type creating more positive ions at the junction.
This widens the depletion region.
Notes: Random topics just for revising some concepts.

## Slide 17: Reverse Current
  A small amount current is generated due to the minority carriers in p and n regions.
  These minority carriers are produced due to thermally generated hole-electron pairs.
  Minority electrons in p-region pushed towards +ve bias voltage, cross junction and then fall in the holes in n-region and still travel in valance band generating a hole current.
Notes: Random topics just for revising some concepts.

## Slide 18: Reverse Breakdown
  If the external bias voltage is increased to a value call breakdown voltage the reverse current can increase drastically.
  Free minority electrons get enough energy to knock valance electron into the conduction band.
  The newly released electron can further strike with other atoms.
  The process is called avalanche effect.
Notes: Random topics just for revising some concepts.

## Slide 19: Diode V-I Characteristic
VI Characteristic for forward bias.
  The current in forward biased called forward current and is designated If.
  At 0V (Vbias) across the diode, there is no forward current.
  With gradual increase of Vbias, the forward voltage and forward current increases.
  A resistor in series will limit the forward current in order to protect the diode from overheating and permanent damage.
  A portion of forward-bias voltage drops across the limiting resistor.
  Continuing increase of Vf causes rapid increase of forward current but only a gradual increase in voltage across diode.
Notes: Random topics just for revising some concepts.

## Slide 20: Diode V-I Characteristic
  Dynamic Resistance:
  The resistance of diode is not constant but it changes over the entire curve. So it is called dynamic resistance.

## Slide 21: Diode V-I Characteristic
VI Characteristic for reverse bias.
  With 0V reverse voltage there is no reverse current.
  There is only a small current through the junction as the reverse voltage increases.
  At a point, reverse current shoots up with the break down of diode. The voltage called break down voltage. This is not normal mode of operation.
  After this point the reverse voltage remains at approximately VBR but IR increase very rapidly.
  Break down voltage depends on doping level, set by manufacturer.
Notes: Random topics just for revising some concepts.

## Slide 22: Diode V-I Characteristic
The complete V-I characteristic curve